SYSTEM CALLS

Socket creation:

        The first step is to call the socket function, specifying the type of communication
        protocol (TCP based on IPv4, TCP based on IPv6, UDP).

int sockfd = socket(domain, type, protocol)
sockfd:- socket descriptor, an integer (like a file-handle)
domain:- integer, communication domain e.g., AF_INET (IPv4 protocol) , AF_INET6 (IPv6 protocol)
type:- communication type
SOCK_STREAM: TCP(reliable, connection oriented)
SOCK_DGRAM: UDP(unreliable, connectionless)
protocol:- Protocol value for Internet Protocol(IP), which is 0. This is the same number which appears on protocol field in the IP header of a packet.(man protocols for more details)
Bind:
     The bind() assigns a local protocol address to a socket. With the Internet protocols,
        the address is the combination of an IPv4 or IPv6 address (32-bit or 128-bit) address
        along with a 16 bit TCP port number.

int bind(int sockfd, const struct sockaddr *addr,
socklen_t addrlen);
After creation of the socket, bind function binds the socket to the address and port number specified in addr(custom data structure). In the example code, we bind the server to the localhost, hence we use INADDR_ANY to specify the IP address.

Listen:
      The listen() function converts an unconnected socket into a passive socket,
        indicating that the kernel should accept incoming connection requests directed to this
        socket. It is defined as follows:

int listen(int sockfd, int backlog);
It puts the server socket in a passive mode, where it waits for the client to approach the server to make a connection. The backlog, defines the maximum length to which the queue of pending connections for sockfd may grow. If a connection request arrives when the queue is full, the client may receive an error with an indication of ECONNREFUSED.

Accept:
     The accept() is used to retrieve a connect request and convert that into a request.
int new_socket= accept(int sockfd, struct sockaddr *addr, socklen_t *addrlen);
It extracts the first connection request on the queue of pending connections for the listening socket, sockfd, creates a new connected socket, and returns a new file descriptor referring to that socket. At this point, connection is established between client and server, and they are ready to transfer data.
Connect:
The connect() function is used by a TCP client to establish a connection with a TCP	server.The function is defined as follows:
int connect(int sockfd, const struct sockaddr *addr,
socklen_t addrlen);
The connect() system call connects the socket referred to by the file descriptor sockfd to the address specified by addr. Server’s address and port is specified in addr.